## Slide 1: TITLE OF THE PROJECT
Name & address of PI and co- PI

## Slide 2: OBJECTIVE AND INTRODUCTION
Objective- How will it benefit to society
Brief introduction of the fabrication device

## Slide 3: NOVELTY
Clearly indicate the novelty

## Slide 4: Process Flow (Example)
Wafer specifications:
Wafer: Si
Wafer type: p-type
Orientation: <100>
Resistivity: 4-7 ohm-cm
RCA cleaning of the wafer
Oxidation: 20 nm thick SiO2 layer to be grown by dry oxidation furnace 4. Measurement of oxide thickness by ellipsometer
100 nm thick Al layer deposition by thermal evaporation system
Spin coating of positive photo-resist (example: SPR 1813)
UV illumination of the sample in DSA through mask with dots of diameter 1mm 8. Exposed sample treated in developing solution (MF319).
Wet etching of Al layer by etchant solution (H3PO4:CH3COOH:HNO3:DI water = 16:1:1:2)
Removal of photo-resist by acetone
Back etching of the sample by 2% HF solution
100 nm thick Al layer deposition at back of the sample by thermal evaporation system
FGA at 420ºC for 20 min

## Slide 5: Process Flow –Schematics (Example)
Please Note :
For thin film, deposition, please mention the thickness
Mention the feature size, pitch dimensions at each fabrication steps of lithography
Final top view of the device is also required
Mention the thickness at each level for deposition

## Slide 6: Infrastructure required from IITBNF
Mention all fabrication and the characterization tools required (Details of R&D infrastructure available at the IITBNF may be found on http://www.iitbnf.iitb.ac.in/iitbnf/index.php/infrastructure?layout=edit&id=18 )
For example :
Oxidation Furnace
Thermal Evaporator
MJB4 lithography

## Slide 7: References (Maximum 10)